## Slide 1: A dynamic Bayesian network approach to forecast short-term urban rail passenger flows with incomplete data Jérémy Roos • Gérald Gavin • Stéphane Bonnevay European Transport Conference 2016, Barcelona

## Slide 2
1. Context and problematic
2. Modelling approach
3. Large-scale experiment
4. Conclusion and references
Contents

## Slide 3: RATP
Main public transport operator in the Paris region
  16 metro lines
  Sections of 2 RER lines (commuter rail)
  8 tramway lines
  More than 350 bus lines
  3 billions travels per year
1. Context and problematic

## Slide 4: Industrial context
Current models: assessment of the long-term effects of infrastructure/transport policy changes
  Models not designed for short-term forecasting
  Unexpected/non-recurrent events not taken into account:
    Service disruptions
    Unplanned closures of stations
    Crowd-attracting events
    …
Diversity of data sources
  Diversity still untapped  partial view of the mobility
  Failures/lack of collection systems  incompleteness
1. Context and problematic

## Slide 5: Problematic
Harnessing of the diversity of data to forecast the short-term passenger flows
  Many applications in transport system management:
    Operation planning
    Passenger flow regulation
    Passenger information
    Analysis of travel bahaviour
    …
  Various methods in the literature but few applications to public transport networks
Necessity to forecast with missing data
  Few methods proposed in a real-time setting
1. Context and problematic

## Slide 6: Bayesian networks
Representation of the conditional dependencies between random variables
Ability to forecast in case of missing data
High modularity
Easy interpretability
2. Modelling approach

## Slide 7: From transport to Bayesian network
Causal relationships between the upstream and downstream flows  derivation of the structure from the transport network
2. Modelling approach

## Slide 8: Extension to dynamic Bayesian networks
Forecasting the future values  extension to the spatiotemporal neighbourhood: each flow at depends on its upstream flows at (e.g. )
2. Modelling approach

## Slide 9: Extension to dynamic Bayesian networks
Consideration of the trend: each flow at depends on its values at (e.g. )
2. Modelling approach

## Slide 10: Integration of the transport service
Relationship between the flows and the transport service
  Inability to fit the large fluctuations without transport service data (e.g. boarding flow in Nanterre-Préfecture station)
2. Modelling approach

## Slide 11: Integration of the transport service
Impact of the waiting times on the boarding flows  transport service variables associated with the stop point at
2. Modelling approach

## Slide 12: Conditional probability distributions
Assumption: linearity of the relationships  description of the conditional distributions as linear Gaussians:
Estimation of , and by maximum likelihood
  Easy with a complete dataset
  Untractable in case of incomplete data
2. Modelling approach

## Slide 13: Learning and inference
Expectation-maximization (EM) algorithm: iterative method for finding the maximum likelihood estimate with missing data
Reduction of the number of arcs  extension of the EM algorithm to its structural version
  Lower computational complexity
  Lower risk of overfitting
Short-term prediction: inference problem
  Exact methods time-consuming
  Approximate methods better suited for real-time predictions (e.g. bootstrap filter)
2. Modelling approach

## Slide 14: Input data
Stations served by Paris metro line 2
3 types of data:
  Ticket validation (35 flows)
  Automatic counts by on-board weighing systems (60 flows)
  Transport service (114 variables)
33 weekdays of March and April 2015, between 7.30 and 9.30 am, per 2 minutes
Missing data rate: 4.8 %
3. Large-scale experiment

## Slide 15: Experimental method
Learning from the first 24 days
  Best empirical results: ,
Test on the last 9 days
  Comparison with 2 partial versions:
    Without transport service
    Without upstream-downstream relationships
  Comparison with 2 naïve methods:
    Historical average
    Last observation carried forward (LOCF)
  Accuracy measure:
3. Large-scale experiment

## Slide 16: Forecasting results
High contribution of the transport service, especially for the train departure flows (e.g. from Blanche station to Place de Clichy station)
Significant improvement when integrating the upstream-downstream relationships
3. Large-scale experiment

## Slide 17: Forecasting results
Overall superiority of the dynamic Bayesian network approach due to the train departure flows
Superiority of historical average for the flows from public to controlled areas
  Flows located at the margins  cannot exploit the full potential of the model
  Regularity of the flows from day to day
3. Large-scale experiment

## Slide 18: Conclusion
Overall effectiveness of the dynamic Bayesian network approach
  Ability to forecast with missing data
  Key role of the transport service
  Necessity to improve the model for the walking flows
Assumption of linearity questionable  what about more sophisticated distributions (e.g. Gaussian mixture models) ?
Stationarity of the structure and the parameters  effectiveness in case of major disruptions ?
High modularity  possibility to incorporate new data sources:
  Temporal factors: trend, month of the year, day of the week…
  External features: weather conditions, sporting or cultural events…
4. Conclusion and references

## Slide 19: References
Haworth, J. (2014) Spatio-temporal forecasting of network data, Doctoral dissertation, University College London.
Friedman, N., Murphy, K., Russel, S. (1998) Learning the Structure of Dynamic Probabilistic Networks, Proceedings of the 14th Conference on Uncertainty in Artificial Intelligence, Madison, 139-147.
Kanazawa, K., Koller, D., Russel, S. (1995) Stochastic simulation algorithms for dynamic probabilistic networks, Proceedings of the 11th Conference on Uncertainty in Artificial Intelligence, Montreal, 346-351.
Koller, D., Friedman, N. (2009) Probabilistic Graphical Models: Principles and Techniques, The MIT Press, Cambridge.
Sun, S., Zhang, C., Yu, G. (2006) A Bayesian Network Approach to Traffic Flow Forecasting, IEEE Transactions on Intelligent Transportation Systems, 7(1), 124-132.
4. Conclusion and references